## Slide 1: Guidance note: Agriculture chapter
EU Agricultural Emission Estimation with N-flow tool and AgrEE tool
NH3, NOx, N2O
NMVOC, PM10, PM2.5, TSP, SO2, CO, BC, Heavy Metals, Dioxins, POPs
CH4
3B Manure Management
3D Agriculture Soils
3Da1, 3Da2b, 3Da2c 3De
3Da2a,3Da3,
3F Field Burnig Agriculture Resisues
3A1 Enteric Fermentation
N-flow tool
AgrEE Tool
Notes: Here a general vie of the AgrEE tool is provided

## Slide 2: Guidance note: Agriculture chapter
Expanding the estimation of air pollutant and GHG emissions already in place through the N-flow tool including other air pollutants and GHG and other agricultural activities
A user-friendly web tool with EU login designed to improve the consistency between air and GHG emission reporting
Based on EMEP/EEA Guidebook 2019 and IPCC Guide 2006
Tier 2 as the main method allowing also the use of Tier 1 method
Developed for Livestock, Agriculture Soils and Field Burning
Provides emissions for all relevant air pollutants from agriculture regulated under the NECD, other air pollutants (PM10, TSP, SO2, CO, Heavy metals, Dioxins, POPs) and greenhouse gases (CH4, N2O)
Possibility to consider the effect of abatement measures
Agricultural Emission Estimation Tool – AgrEE Tool
Notes: Here a general vie of the AgrEE tool is provided

## Slide 3: Guidance note: Agriculture chapter
AgrEE Tool
What in common with N-flow tool– Tier 2 method in focus
Both tools provide the estimation of NH3, NOx, N2O applying the EMEP/EEA Tier 2 method for: 3B Manure Management 3Da2a Manure Applied to Soils, 3Da3 Urine and Dung Deposited by Grazing Animals, and 5B2 Biological Treatment of Waste (calculations are already inserted in the AgrEE tool) Developed for 13 main livestock categories To facilitate the work of inventory compilers the AgrEE tool uses the same terminology for the activity data and emission factors as in the N-flow tool. Results on air pollutant emissions are practically the same as the AgrEE tool tries to provide as much as possible freedom in the uses of decimals.
Notes: AgrEE Tool development is based in the n-flow tool and has chosen to apply the same terminology since the MS are using the N-flow tool in the preparation of their inventories. So the AgrEE tool provides the same outputs as the N-flow tool for 3B (Manure Management=, 3Da2a (Manure applied to soils) and 3Da3 (Urine ans Dung Deposited by Grazing Animals). Estimation of emissions from sector 5B2 are also calculated but at this stage they are not displayed.

## Slide 4: Guidance note: Agriculture chapter
AgrEE Tool
What is additional – Tier 2 method in focus | 
Applying Tier 2 method the AgrEE tool additionally estimates emissions for: 3B Manure Management - NMVOC, PM10, PM2.5, TSP 3D Agricultural Soils 3Da1 Inorganic Fertilisers - NH3 3De Cultivated crops - NMVOC 3Dc Farm level agricultural operation PM10, PM2.5, TSP 3F Field Burning of Agricultural Residues - NH3, NOx, NMVOC, TSP, PM10, PM2.5, SOx, BC, CO, Heavy Metals, POPs (EDGAR emission factors are used) Manure Management and Enteric Fermentation - CH4 Includes country specific livestock structure (subdivision) – e.g 34 subdivisions for IE, 24 subdivisions for DK, LU | 
Cattle (upon age)
Dairy cattle (e.g lactating)
Other cattle (e.g suclking cows)
Heifers (e.g dairy, other)
Bulls (e.g fattening)
Calves (e.g slaughter calves)
Sheep (e.g ewes, lamb)
Swine (e.g boars)
Sows (e.g breeding sows)
Goats (e.g mature, kids)
Other animals (e.g ostrich)
Notes: Here the focus is on additional estimations when using the AgrEE tool and when applying Tier 2 method.
Other air pollutants (NMVOC, PM10, PM2.5, TSP, SO2, CO, BC, Heavy Metals, POPs) emissions can be estimated
Also other sectors are included
Livestock subdivisions reflect the MS livestock profiles

## Slide 5: Guidance note: Agriculture chapter
AgrEE Tool
More features
Compact input templates (activity data/emission factors) – user can download the input template (excel format), fill it and upload in the tool – one click to perform calculations (for all years if selected) Activity data in common assigned to all pollutants within the same method Possibility to insert reduction factors for NH3 emissions from livestock (simple approach) or the user can insert directly in the tool the average emission factors calculated separately Calculation of methane emission factors – comparison with default IPCC values Enable extracting results conform the required Annex 1 template – aggregated emissions if more that one subcategory/subdivision is selected Interactive analysis on trends, relative contributions (categories/sectors), livestock profiles, results comparison, emissions comparison versus a base year, uncertainty displaying together with the estimated emissions