## Slide 1: GAINS emission projections for the EU Clean Air Policy Package Work in 2014-2015
Zbigniew Klimont (klimont@iiasa.ac.at)
Task Force on Emission Inventories and Projections Projection Expert Panel Meeting Milan, Italy, May 11-12, 2015

## Slide 2: TSAP related work in 2014/15
New analyses for Working Party on Environment (WPE) of the European Council:
  Incorporation of new statistical information
  Updated NEC proposal
For the European Parliament:
  Interactions with recent climate policy decisions

## Slide 3: Contributions to the emission reductions of the re-optimized scenario meeting CAPP targets [WPE, 2014] (relative to 2005 emissions)
Source: GAINS model – TSAP #16

## Slide 4: Objectives of bilateral consultations with MS conducted under the auspices of the WPE
Eliminate potential misunderstandings (e.g., in model results, input data, or national statistics)
Spot and correct obvious mistakes in input data
Identify differences in perspectives on future development, and assess their relevance on overall outcomes (i.e., national emission ceilings or relative changes in emissions over time)
Summarize and report to Commission and Member States

## Slide 5: Bilateral consultations with all 28 MS
Bilateral contacts with all 28 Member States
  24 meetings at IIASA, 1 video-conference, 3 MS via e-mail exchange
More than 110 experts involved
Completed in July 2014
Results were incorporated into GAINS thereafter
Minutes of meetings provided in updated report TSAP #13 1)
Implementation in GAINS documented in TSAP #14, #16 1)
1) The reports available from the GAINS web: http://gains.iiasa.ac.at (see Policy applications)

## Slide 6: Changes in emission inventories for 2005 between 2012 and 2014 submissions

## Slide 7: Changes in emission inventories for 2005 between 2012 and 2014 submissions

## Slide 8: Frequent reasons for discrepancies of 2005 emission inventories
Differences in source coverage (e.g., agricultural soils, burning of agricultural waste, etc.).
Different inventory methods for some sources (PM2.5, NH3) (GAINS uses principally Tier 2 attempting to reflect on national circumstances, but some MS still employ Tier 1 that ignores local conditions)
Discrepancies between national energy statistics used for emission inventories and what has been submitted to EUROSTAT
Variations in emission factors due to national circumstances;
Ongoing further improvements in national inventories; GAINS has been adjusted to 2014 or, if provided, 2015 submissions

## Slide 9: Overall, good match of updated GAINS 2005 inventories with national 2014 submissions – with exceptions
 | Difference EU-28 | # of countries with difference <5% | # of countries with difference >5%
SO2 | -0.4% | 27 | 1
NOx | -0.4% | 22 | 6
PM2.5 | +13% | 16 | 12
NH3 | +2% | 19 | 9
VOC | +3% | 17 | 11

## Slide 10: Frequent reasons for differences of (baseline) emission projections for 2030
Different activity projections
Already agreed legislation (e.g., Stage IV for non—road machinery) not always taken into account in national projections
Different assumptions on the effectiveness of Euro 6, the timing of introduction, and the turnover rate of the vehicle stock
Many countries assume no change in average emission factors from the ongoing renewal of installations (e.g., for residential combustion and the solvents sector)
Some countries assume fixed relation between GDP and (the quantity of) personal products containing solvents (hairsprays etc), GAINS assumes saturation at high income levels.

## Slide 11
Many MS have different perspectives on the future evolution of economic activities, energy use, transport demand and agricultural activities.
19 Member States provided (partial) national projections;
International consistency of national projections should be assessed.
Projections of future activities

## Slide 12: Examples of national livestock projections against CAPRI model used in WEP, 2014

## Slide 13: Future mitigation potentials
Activity projections (higher activity levels than assumed in PRIMES/CAPRI)
Enforcement of the (already existing) ban of agricultural waste burning is considered as unrealistic in some MS
Different expectations for the Ecodesign directive – new standards as of 2022

## Slide 14: Comparison of optimized reduction commitments considering national projections and the WPE2014 scenarios (relative to 2005)
Chart: 
| SO2 | NOX | PM2.5 | NH3 | NMVOC
National | -68 | -61 | -30 | -6 | -36
WPE | -2 | -2 | -4 | -3 | -2
MFR-National | -82 | -73 | -62 | -33 | -59
MFR-WPE | 0 | 0 | -1 | -2 | 0

## Slide 15: Comparison of optimized reduction commitments considering national projections and the WPE2014 scenarios (relative to 2005)
Chart: 
| SO2 | NOX | PM2.5 | NH3 | NMVOC
National | -68 | -61 | -30 | -6 | -36
WPE | -2 | -2 | -4 | -3 | -2
MFR-National | -82 | -73 | -62 | -33 | -59
MFR-WPE | 0 | 0 | -1 | -2 | 0
Chart: 
| SO2 | NOX | PM2.5 | NH3 | NMVOC
National | -68 | -61 | -30 | -6 | -36
WPE | -2 | -2 | -4 | -3 | -2
MFR-National | -82 | -73 | -62 | -33 | -59
MFR-WPE | 0 | 0 | -1 | -2 | 0
OPT-NAT | 4 | 7 | 8 | 8 | 16
OPT-WPE | -3 | 1 | 1 | 2 | -3
Achieved by2012

## Slide 16: Comparison of optimized reduction commitments considering national projections and the WPE2014 scenarios (relative to 2005)
 | WPE 2014 | NATIONAL PROJECTIONS |  |  | WPE 2014 |  | 
 | Re-optimized | CLE | MTFR | Average margin of the re-optimized scenario to MTFR | CLE | MTFR | Average margin of the re-optimized scenario to MTFR
SO2 | -78% | -68% | -82% | +4% | -70% | -82% | +5%
NOx | -66% | -61% | -73% | +9% | -63% | -73% | +9%
PM2.5 | -55% | -30% | -62% | +10% | -34% | -63% | +12%
NH3 | -27% | -6% | -33% | +17% | -9% | -35% | +22%
VOC | -43% | -36% | -59% | +26% | -38% | -59% | +27%
19 EU countries provided national projections that were implemented in GAINS

## Slide 17: The updated proposal for National Emission Ceilings in 2030 (EU-28, emissions relative to 2005)
 | 2012 | Original Commission proposal for 2030 |  | WPE update | 
 |  | Baseline | Proposal | Baseline | Proposal
SO2 | -48% | -73% | -81% | -74% | -81%
NOx | -27% | -65% | -69% | -63% | -65%
PM2.5 | -12% | -27% | -51% | -32% | -54%
NH3 | -5% | -7% | -27% | -8% | -25%
VOC | -24% | -41% | -50% | -40% | -46%

## Slide 18: Conclusions
Overwhelming participation of all MS in the bilateral consultations, very constructive attitude.
The emission reduction requirements proposed by the Commission remain technically feasible for the PRIMES 2013 REFERENCE scenario (with one exception).
Updated NECs have been produced for WPE; costs decline by one third. The new ceilings are feasible also for the national projections (with one exception)
Quality and international consistency of emission inventories is critical for cost-effectiveness approach. Are current quality control procedures sufficient?