## Slide 1: The UK Emissions Projections
Yvonne Pang
TFEIP/EIONET Annual Meeting - Projections Expert Panel
12th May 2015

## Slide 2: What’s in this presentation
Background on UK projections
Applications of the UK projections
Sector example: Road transport projections

## Slide 3: Background on UK projections
  The UK National Atmospheric Emissions Inventory (NAEI) programme is funded by
  The NAEI project team is made up of a consortium led by Ricardo-AEA
  supported by the Centre for Ecology and Hydrology, Rothamstead research, Aether, SKM-Enviros and AMEC

## Slide 4: Background on UK projections – Coverage
  The UK projections model calculates projected emissions for
  NOx, SO2, NH3, NMVOC, PM10, PM2.5, BC, CO, benzene, arsenic, cadmium, nickel, lead, benzo[a]pyrene
  2015, 2020, 2025, 2030 (Road Transport out to 2035)
  Same detailed disaggregation as the UK National Atmospheric Emission Inventory (NAEI)

## Slide 5: Background on UK projections – Data Sources
  The key input data include:
  UK National Atmospheric Emission Inventory (NAEI) - baseline
  The Department of Energy and Climate Change (DECC) Energy and Emissions Projections model (EEP)
  The Department for Transport (DfT) traffic forecasts
  Updated projections of livestock numbers and fertiliser use to 2030 using data derived from the FAPRI agricultural model by Queens University Belfast on behalf of Defra
  Process operators and trade associations

## Slide 6: Background on UK projections – Methods and Assumptions
  Methodology
Eproj = (ANAEI Baseyear * AD) * EFproj
Where E = emission, A = activity, AD = activity driver and EF = emission factor
  General Assumptions
  Only consider firm and funded polices as described in DECC EEP
  All operators comply with legislation
  New abatement is applied to sources in order to meet the limits imposed by regulations or in response to the impacts of trading mechanisms

## Slide 7: Applications of the UK projections
  To support UK Government with
  Reporting and tracking progress towards emission reduction targets (NECD and Gothenburg Protocol)
  Assessing compliance with the EU Air Quality Directive
  Formulation and assessment of national policies on air pollution
  UK Projections are used in a wide range of policy tools:
  Pollution Climate Model
  Multi-Pollutant Measures Database (MPMD)
  UK Integrated Assessment model (national and urban scale modelling)
  Regional scale air quality modelling

## Slide 8: Good Practice
  Working closely with other stakeholders and AQ community
    Make additional information available for AQ modellers
    To do projection on a consistent basis
To be launched on the NAEI website in the future 

## Slide 9: Sector example: Road transport projections

## Slide 10: Overview (1)
  Pollutants coverage
    NOx, NMVOCs, SO2, NH3, PM10, PM2.5, benzene, CO, metals
    non-CO2 GHG (CH4, N2O)
  Vehicle types
    Cars, LGVs, Rigid and artic HGVs, Buses and coaches, Motorcycles
  Euro standard system (up to Euro 6/VI)

## Slide 11: Overview (2)
  Emissions from each vehicle type =
  Emission factor (g/km) x Projected activity (vehicle km travelled)
EMEP/EEA Emission Inventory Guidebook / COPERT 4
DfT/TRL (2009)
Fleet composition:
By fuel type
By age mix  Euro standard
By engine size/ vehicle weight
By technology

## Slide 12: Traffic projections – Data Sources
  Great Britain
    Department for Transport (vehicle-km)
    Up to 2035 (recently 2040)
    By vehicle, road, area type and Government Office Region
    Derived from the DfT’s National Transport Model based on UK transport policy
  London
    Transport for London
    Growth factors for 2021 and 2031
  Northern Ireland
    Assume same as GB’s growth rates

## Slide 13: Fleet composition assumptions
  Fleet turnover model  proportion of vehicle km by Euro Standard
    Vehicle sales projections
      DfT for Cars and LGVs - Conventional (diesel/ petrol), full hybrid, plug-in hybrid, Electric
      Correlation b/c historical vehicle sales (and total vehicles on road) against vehicle-km travelled data  Use traffic projection as a proxy to project vehicle sales
    Vehicle survival rates
    Relative mileage with age
  Fleet composition data for London – Transport for London
    Taking into account the impact of Low Emission Zone (LEZ), TfL Bus measures, Taxi age limit

## Slide 14: Sensitivity Analysis
  Varying input assumptions e.g. traffic growth, diesel penetration rate, NOx assumptions for Euro 6 diesel cars and LGVs
Chart: Urban NOx emissions (in ktonnes) from all vehicles
| 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035
Scenario 1 | 134.6638 | 132.0006 | 127.8475 | 120.3121 | 109.5042 | 99.4024 | 90.4532 | 82.7965 | 76.1474 | 70.3396 | 65.2868 | 60.8317 | 57.1002 | 53.6805 | 50.8512 | 48.97 | 47.6278 | 46.7038 | 46.0533 | 45.5833 | 45.244 | 45.0063 | 44.8724 | 44.7989
Scenario 2 | 134.6638 | 132.0006 | 127.8475 | 120.3121 | 109.5042 | 99.4024 | 89.3411 | 79.641 | 71.0294 | 63.5441 | 57.0084 | 51.2196 | 46.3259 | 41.8308 | 38.0955 | 35.4493 | 33.4522 | 32.0085 | 30.979 | 30.2812 | 29.81 | 29.504 | 29.3392 | 29.2613
Scenario 3 | 134.6638 | 132.0006 | 127.8475 | 124.9414 | 122.4234 | 120.5076 | 115.2456 | 108.3794 | 102.0592 | 96.4663 | 91.7687 | 87.5665 | 83.8799 | 80.2394 | 76.8525 | 74.2953 | 72.1106 | 70.3397 | 68.9608 | 67.9228 | 67.1828 | 66.7 | 66.4393 | 66.3283

## Slide 15: Output
  Emissions projections by vehicle type and road type
  Fleet composition projections data
    NAEI Website (http://naei.defra.gov.uk/)
    Input for the Emission Factors Toolkit for local air quality assessment http://laqm.defra.gov.uk/review-and-assessment/tools/emissions-factors-toolkit.html

## Slide 16: Yvonne Pang
Ricardo-AEA Ltd
The Gemini Building
Fermi Avenue
Harwell, Didcot,
OX11 0QR
01235 75 3444
yvonne.pang@ricardo-aea.com
www.ricardo-aea.com
Thank you

## Slide 17
    Emission Factors Toolkit for local air quality assessment
    http://laqm.defra.gov.uk/review-and-assessment/tools/emissions-factors-toolkit.html